## Slide 1: Sustainable Design
Team 1

## Slide 2: Foundational Materials
For the construction of our work centre we have a few options:
Timber – this provides a cheap and strong foundation plus framework for our building as it’s almost as good as steel beams and reduces carbon footprint by upto 40% and is easy to acquire.
Ferrock- a revolutionary discovery from 2002, that completely traps co2 and acts as a cement. This would be great if we didn’t have a budget as it’s structural integrity even exceeds that of regular concrete whilst also making us very sustainable as it’s completely carbon negative and will last a very long time.
K-Briq Blocks – This is a brick alternative to creating the framework is possibly the single most sustainable material we could use due to it being 100% recycled and are much easier to use causing a reduction of 90% in energy usage whilst preparing each brick.
After further consideration following the pre-existing materials used on campus, K-Briq Blocks would fit the structure a lot more seamlessley and provide us with the best benefits, some of which are :
Compressive strength of 30 N/mm², water absorption of 2%, and durability rating of F2.
Contains under 20g CO₂e per unit—producing up to 95% less embodied carbon than a standard clay brick.
Made from near 100% recycled debris (such as crushed brick, mortar, gravel, and plasterboard).
Unfired and cured at low temperatures, which avoids high-energy kiln firing.
In addition to this, we don’t need to paint the exterior as clifton campus uses the bricks as the aesthetic.
https://www.kenoteq.com/k-briq

## Slide 3: Walls
For walls we also have a variety of materials that could be effective in increasing our stability, but one seems perfect for our goal:
Hempcrete- this is a bio composite compound featuring plants and lime binders. This could be used for infills, and thermal wrapping. This means that it’s practically a sustainable insulation for our walls, but it also provides sound reducting walls, and regulated internal humidity levels creating a better and more comfortable work environment.
We are likely to use a mix of Hempcrete and K-Briq Blocks in development of this building. Hempcrete is likely gonna be used in unison with k-Briq Blocks as they lack structural integrity, in order to provide the vast benefits such as:
"Absorbing and releasing moisture vapor naturally, helping regulate indoor humidity (typically between 40% and 60%) and preventing condensation or black mold. "
"Providing both thermal mass and insulation, keeping buildings warmer in the winter and cooler in the summer while dampening sound. "
"Fire, Pest, & Rot Resistant: Due to the high alkalinity of the lime binder, it naturally repels mold, insects, rodents, and fire."
"Carbon-Negative: Hemp plants absorb high amounts of CO₂ while growing, and the lime binder continues to carbonate over time, locking away more carbon than is emitted during its production."
https://en.wikipedia.org/wiki/Hempcrete
https://naturalbuildingstore.com/product-category/hempcrete/
https://www.ukhempcrete.com/building-with-hempcrete/
https://www.ukhempcrete.com/?faq-group=about-hempcrete
https://www.youtube.com/watch?v=IsM7OqEOiFM&t=65

## Slide 4: Interior and finishing materials
In order to raise our sustainability on the certification, we need to follow standards provided by BREAM or LEAD.
Flooring- Any recycled carpet tiles. These give us a 100% recycled flooring , whilst also being good for our work environment. This also provides a continuous design along the floors and can be separated easily, or even cut into the perfect dimensions prior to being delivered
Partitions- we could utilise demountable glass walls. This will maximise natural light, minimise drywall waste if we ever have repairs or expansions, and mostly just reduces carbon footprint by eliminating the possibility of negative materials being used as drywall.
Coating-Zero VOC paint. This paint is incredible compared to others minimising airborne chemicals by upto 90% upon application, and makes sure the environment is ready to work, and ecosystems aren’t affected

## Slide 5: Sustainable Technology